## Slide 1: Biomechanical modeling of Tissue perfusion in Decellularized and Native liver
Kenichiro nishii1, erik brodin1, greg reese1, emma moran2, Jessica L. Sparks1
SMB 2017
1Miami University, Oxford, OH
2Wake forest institute for regenerative medicine, Winston Salem, NC

## Slide 2: background

## Slide 3: Model system: Decellularized Liver
Baptista PM et al, (2011) Hepatology 53, 604-617.
Notes: Whole organ decellularization is a technique to eliminate all cellular components to create a scaffold that retains the liver’s original extracellular matrix architecture and vascular network. Image (A, B) shows ferret liver in original state (far left), and progressive loss of cells until empty scaffold is created.
This method is used to generate scaffolds for liver bioengineering. Serves as the model system for the present study.

## Slide 4
Mechanical forces have important effects on liver cells
The mechanical environment in perfused decelllularized scaffolds is largely unknown
Guiding hypothesis:
  Multiscale computational modeling can be used to assess and to optimize mechanical forces in perfused scaffolds
Goal:
  To quantify the mechanical microenvironment in perfused decellularized liver, using a combined experimental/ computational approach
1-10 cm
1-10 mm
100 – 1000 μm
1-100 μm
Nishii K et al. Journal of the Mechanical Behavior of Biomedical Materials 57 (2016) 201-214.
Notes: Describing the mechanical environment in liver is a multiscale problem.
Understanding/controlling these forces is important for generating functional, viable tissue.
(This work was published in 2016, citation below.)

## Slide 5: methods

## Slide 6: experiments: Parenchymal fluid pressure (PFP)
Right lobe isolated from native and decell ferret livers
Scaffolds perfused via the portal vein at 3, 6, 9, 12 ml/min
PFP measured with needle-guided transducer tipped catheter
Ex-Situ Measurements
In-Situ Measurements
PFP was measured in 5 rats
6 locations per animal
Physiological flow rate
Protocol reviewed and approved by ACUC at WFUHS.
Moran et al. (2012) Biomed Sci Instrum 48, 303-309.
Notes: PFP is analogous to interstitial fluid pressure.

## Slide 7: Experiments: pressure drop across entire scaffold
Inlet pressure measured near portal vein cannula for 3,6,9,12 mL/min
Recorded with and without liver attached, to account for resistance due to tubing/hardware
Pressure drop used to approximate net resistance:
Notes: The total resistance across the liver, estimated from the pressure drop experiments, was used to validate the optimized resistance parameters of the electrical analog model, which we will discuss next.

## Slide 8: Overview of computational modeling approach
Organ Scale Model of Liver Hemodynamics
Calculates pressure and flow at EACH GENERATION of the liver vascular tree.
Tissue Scale Model of Lobule Perfusion
Calculates PFP, fluid velocity, and ECM stress/strain throughout lobule
tPV
pre-tPV
CV
Analogy to electrical circuit:
Voltage ~ Pressure
Current ~ Flow
Debbaut et al. IEEE Trans Biomed Eng 2012;59(12):3293-3302.

## Slide 9: Tissue Scale Model of Lobule perfusion: Finite Element (FE) Model
Two FE models created in Abaqus (Native, Decell)
Common geometry used for both models
178,283 elements in quarter-lobule model
Simulations run via Ohio Supercomputer Center
Notes: simulation run time = 12 hours

## Slide 10: FE Material properties
Deformable Solid Component
Rate-Indepependent Tissue Response: Linear Elasticity
Rate-Dependent Tissue Response: Viscoelasticity
  Modeling liver tissue parenchyma as a biphasic material, consisting of fluid and solid components, much like a sponge.
Fluid Component
Darcy’s Law
Governs fluid flow through solid matrix
Movement of fluid through tissue is driven by pressure and depends on permeability

## Slide 11: FE Material properties
Calculated from density, viscosity, void ratio, and sinusoid geometry
From microscopy image analysis (segmentation of void and solid regions in decellularized liver)
Decellularized liver permeability is 5.6 times greater than native
From previous micro-scale experiments on native and decell liver
(Evans et al. (2013) Biomech Mod Mechanobiol 12(3) 569-580.)
Notes: Void Ratio = Vv/Vs
Hydraulic conductivity, K = permeability (m^4/Ns) * specific weight (kg/m^3 * m/s^2)

## Slide 12: Boundary Conditions
CV surface
pressure = 0
(sink)
Terminal PV pressure from EA model (magnitude above CV pressure)
Pre-terminal PV pressure
from EA model (varies along vessel length)
Symmetry
(X plane)
Symmetry (Y plane)
Notes: To avoid adjacent nodes between tPV and pre-tPV having multiple boundary conditions assigned, a linear relation was used to model pressure variation along length of pre-tPV in z direction. Consistent with reported patterns of linearly decreasing hydrostatic pressure in microvasculature (Koeppen and Stanton 2010).
Figure shows the linear relation for dcellularized liver FE model 9 mL/min case
BCs in bold vary depending on flow rate and native vs decell state.
Assumed uniform expansion in axial direction, no expansion in longitudinal (z) direction, consistent with prior studies (Bonfiglio et al. 2010).

## Slide 13: Results

## Slide 14: experiments: Parenchymal fluid pressure (PFP)
Ex-Situ Measurements
In-Situ Measurements
In-situ Group | Ex-situ Group | p-value
Right lobe in-situ | Native ex-situ: 3 ml/min | .372
 | Native ex-situ: 6 ml/min | .002*
 | Native ex-situ: 9 ml/min | .000*
 | Native ex-situ: 12 ml/min | .000*
 | Decellularized ex-situ: 3 ml/min | .034*
 | Decellularized ex-situ: 6 ml/min | .122
 | Decellularized ex-situ: 9 ml/min | .292
 | Decellularized ex-situ: 12 ml/min | .527
PFP: 2.86 ± 1.04 mmHg
Linear correlation between PFP and flow rate.
Decellularized liver PFP is lower than its native counterpart.
Notes: Suggests resistance is decreased by decellularization
Suggests resistance is decreased by decellularization 𝑅=∆𝑃/𝑄

## Slide 15: Tissue Scale Model of Lobule perfusion: Results for native liver
Fluid velocities highest near vascular inlet/outlet channels.
Pressure shows sigmoidal decrease from inlet to outlet.
avg = 609 μm/s
avg = 10.2 mmHg
avg = 7.2 μm
Notes: Results shown for 9 mL/min flow rate

## Slide 16: Tissue Scale Model of Lobule perfusion: Results for decellularized liver
Same trends, but much lower pressures
avg = 618 μm/s
avg = 1.89 mmHg
avg = 6.3 μm

## Slide 17: validating the tissue scale FE model output
Experimental Perfusion Rates:
Average FE model pore fluid pressure compared with measured PFP
Physiological Perfusion:
Averge pore fluid velocity (native model) = 278 μm/s
Measured plasma velocity in rat sinusoids = 100-750 μm/s
(Koo and Liang (1979) J Physiol 295, 191-199)
Flow Rate (mL/min)
3
6
9
12
PFP (mmHg)
4
8
16
12
20
Native
Decell
Hydraulic conductivity
Native model: K= 1.85 x10-6 m/s
Calculated from fluid properties (ρ,μ), void ratio, and vessel geometry - not optimized!
Literature values: K = .24 x 10-6 to 9.9 x 10-6 m/s
Notes: Three validation strategies indicated good agreement between the FE model predictions and literature/experimental results.
experimental measures of parenchymal fluid pressure (PFP)
For (1), FE model pore fluid pressures were calculated along 3 parallel paths running from the pre-terminal portal vein to central vein. Results of the three paths were then averaged, for comparison with experimental measurements. Model results showed good agreement with our experimental PFP measurements.
(2) independent measures of plasma fluid velocity
When physiological flow rate was applied to the native model, the average model-predicted pore fluid velocity is within the reported range of plasma velocity measured in rat sinusoids
(3) Our calculated model hydraulic conductivity (e.g. permeability) for native liver (1.85 x 10-6 m/s) is in good agreement with the reported range in literature (0.24x10-6 to 9.9x10-6 m/s) (Kerdok, 2006; Debbaut et al., 2012)

## Slide 18: conclusions / Applications to Cancer

## Slide 19: Conclusions
We developed and validated a multiscale computational model of decellularized liver perfusion
We can use the model to
  understand the mechanical forces in perfused decellularized scaffolds
  test the effects of different mechanical environments on cell seeding, growth, and organization of functional bioengineered liver tissue
  optimize perfusion bioreactor conditions
This model system
(scaffold + cells + bioreactor + computational model) is also being used to study the process of colon cancer metastasis to the liver.
Nishii K et al. Journal of the Mechanical Behavior of Biomedical Materials 2016; 57 :201-214.

## Slide 20: Application to Cancer metastasis: work in progress
Flow stagnates within tumor (left); Strains spike at tumor periphery (right)
“Tumor” path
“No tumor” path
“Tumor” path
“No tumor” path
Notes: 400 micron (“medium”) diameter tumor, considered as net pressure source (release of fluid from necrotic core exceeds uptake of fluid by cells in the viable rim).
Ran models for high and low tumor permeability conditions, results here shown for high permeability.
Line plots shown for path taken from pre-terminal portal vein to central vein. Two paths, one through normal parenchyme (“no tumor” path) and one through tumor (“tumor” path). See red lines with arrows on top left figure.
Left side shows fluid velocity across the lobule. For “no tumor” path, flow velocity increases approximately exponentially from portal vein to central vein. For “tumor” path, flow stagnates within tumor, then fluid velocity increases abruptly just outside tumor margin.
Right side shows strain across the lobule. For “no tumor” path, strains are relatively steady at about 3%, then decrease near central vein. For “tumor” path, strains increased sharply at the tumor boundary to a peak value of 9%, highest value observed in the conditions we tested.

## Slide 21: acknowledgments
Kenichiro Nishii
Greg Reese, PhD
Emma Moran, PhD
Shay Soker, PhD
Pedro Baptista, PhD
Doug Evans, MS
Miami Redhawk Cluster
Ohio Supercomputer Center
Funding sponsors:
  DHHS 5R01CA180149-02
    USC Subaward 45391782
  Dept. of Chemical, Paper, and Biomedical Engineering, Miami University

## Slide 22: Biomechanical modeling of Tissue perfusion in Decellularized and Native liver
Kenichiro nishii1, erik brodin1, greg reese1, emma moran2, Jessica L. Sparks1
1Miami University, Oxford, OH
2Wake forest institute for regenerative medicine, Winston Salem, NC
Thank you!